## Slide 1
AUGRADE
Augrade GNN
Layer-blind vector classification with HATCH-IoU as supervision.
Malachi Mabie · Mabie Industries · for Krish, Augrade
DXF_Primitive_to_Polygon · gnn_plan/

## Slide 2
The problem
67,000 primitives. 111 layers. No reliable layer names. No grouping metadata.
Recover walls, columns, curtain walls — and the supervision signal
that lets us keep doing it as drafters and conventions drift.
Augrade · GNN presenter · M. Mabie
02 / 09

## Slide 3
The bet
HATCH companion layers are hidden ground truth.
A graph-recovered polygon's IoU against the * HATCH boundary on its
companion layer catches shape correctness — which the source-entity
coverage proxy misses by construction.
Already shown on real data: snap × joint grid search ranked by HATCH-IoU + coverage.
Augrade · GNN presenter · M. Mabie
03 / 09

## Slide 4
The approach
· Vector first. Layer names are provenance only.
· Heterogeneous graph: primitives, supervectors, faces, annotations.
· Sparse pair-relation baseline with conformal review bands.
· Small GNN only on the residual local features cannot explain.
· Validators stay deterministic. They decide what may auto-apply.
Augrade · GNN presenter · M. Mabie
04 / 09

## Slide 5
What's already shown
Cross-layer pooling is real.
A-GLAZING MULLION (LINE-only) and A-GLAZING-MULLION (LWPOLYLINE-only) are
the same physical mullions at ~97% spatial overlap.
Merges decompose into two stages.
29 / 29 curtain-wall merges are programmatic from provenance alone.
Only 1 / 28 wall merges are.
Snap and joint are independent knobs.
Pareto front: T-junction coupling (joint > 0) is the load-bearing change;
snap is robust across [0.25, 0.75] once joints are explicit.
Augrade · GNN presenter · M. Mabie
05 / 09

## Slide 6
From core model to subagent
One encoder. Many small heads. Each head a tool a frontier model can call.
Core encoder
SSL on HATCH-IoU
+ rewrite contrast.
Frozen after Phase 4.
Task head
Linear or small MLP.
Trained on programmatic
or expert labels.
Calibration
Conformal bands on
drawing-level holdout.
Auto-accept / route.
Tool surface
JSON in / JSON out.
Idempotent.
Frontier model calls it.
The frontier model spends tokens on judgment — reading residual reports,
proposing rules, deciding what to promote into deterministic code —
not on rediscovering geometry the engine already computed.
Augrade · GNN presenter · M. Mabie
06 / 09

## Slide 7
Ninety days
W1 – 4
Graph export + annotation alignment.
M1 – M3
W5 – 8
Sparse calibrated baseline with conformal bands.
M4
W9 – 12
Rewrite-stability tests. GNN only if a residual remains.
M5 (conditional)
Gate at month 3: ≥ 1 relation baseline calibrated, rewrite report exists, validators still own truth.
Augrade · GNN presenter · M. Mabie
07 / 09

## Slide 8
Open questions
1.
At what grain does the annotation pipeline produce labels — primitive, supervector, relation, or edit-event?
2.
Which constraints get first-class deterministic validators — code/compliance, structural, MEP clearance, fire-rating, accessibility?
3.
Which authored rewrites are safe to collapse, and which are family-conditioned — hatch ↔ outline, carrier swap, collinear split, schema remap?
Augrade · GNN presenter · M. Mabie
08 / 09

## Slide 9
Substrate first.
Frontier intelligence borrowed.
Validators decide truth.
Malachi Mabie · Mabie Industries
DXF_Primitive_to_Polygon · gnn_plan/